## Slide 1
CMP720 Embedded System Design — Spring’26
EdgeRAG
Offline Retrieval-Augmented Generation
on Resource-Constrained Simulated ARM Architectures
Hüseyin Eren Doğan | N25123065
Hacettepe University | Aselsan

## Slide 2
Agenda
01
Overview & Motivation
The cloud dependency problem
02
Problem Definition
Objectives, constraints & success criteria
03
Related Work
RAG, edge LLMs, vector DBs, QEMU
04
Methodology
Architecture, MoC, memory management
05
Evaluation Plan
Metrics, dataset, experimental conditions
06
ESD Considerations
Security, reliability, scheduling

## Slide 3
01 — Overview & Motivation
"Modern AI question-answering depends entirely on cloud connectivity —
but many critical environments can't or won't connect."
🔌
Air-Gapped Networks
Defense, industrial IoT, remote infrastructure — no internet access at all.
🔒
Privacy-Critical Systems
Medical devices, legal analysis — data must never leave the device.
⚡
Energy-Constrained Edge
Constant cloud round-trips drain power on remote sensors and robots.
→ EdgeRAG: a fully offline RAG pipeline that runs on constrained embedded hardware — no cloud required.

## Slide 4
02 — Problem Definition
Target Platform
▸ QEMU — ARM Cortex-A53 (AArch64)
▸ Ubuntu 22.04 LTS (minimal)
▸ 2 GB RAM (hard ceiling)
▸ 2 virtual CPU cores @ 1 GHz
▸ No network access (-net none)
▸ Phi-3 Mini Q4_K_M GGUF
▸ FAISS flat L2 index
▸ LangChain orchestrator
System Objectives
O1
Latency
≤ 60 s
end-to-end per query
O2
Memory
≤ 1.8 GB
peak RAM across stages
O3
Reliability
0 OOM
failures on test set
O4
Throughput
≥ 0.5 t/s
token generation rate
O5
QA Quality
F1 ≥ 0.40
Recall@3 ≥ 0.65
✓ Success = ≥ 95% queries completed without OOM, within latency budget, meeting QA thresholds

## Slide 5
03 — Related Work
RAG (Lewis et al., 2020)
• Non-parametric memory + LLM generation
• Grounded answers without larger models
• Gap: assumes GPU / server hardware
Quantization — QLoRA / GGUF
• 4-bit quant: 4× memory reduction
• llama.cpp: CPU-only GGUF inference
• Enables Phi-3 Mini on ≤ 2 GB RAM
Edge AI (Lin & Chen, 2023)
• On-device LLM inference benchmarks
• 1B models viable at 4 GB RAM baseline
• Feasibility baseline for EdgeRAG
FAISS & QEMU
• FAISS: CPU-optimised vector retrieval
• Flat L2: predictable d×n×4 bytes memory
• QEMU: enforces hard resource limits
Positioning: EdgeRAG is an extension — combining RAG + GGUF quantization + FAISS in a novel offline embedded pipeline not yet benchmarked at this scale.

## Slide 6
04 — Methodology: System Architecture
Two-phase pipeline — offline ingestion (left) runs once; online inference (right) runs per query within the QEMU 2 GB envelope.
IngestionModule
RAM: ~100 MB
PDF/text → chunks (256 tok, 32 overlap) → disk
EmbeddingModule
RAM: ~300 MB
MiniLM-L6-v2 → 384-dim vectors → FAISS index → disk → unload
RetrievalModule
RAM: ~80 MB
Load FAISS index → embed query → top-k=3 chunks
GenerationModule
RAM: ~1.4 GB
Load Phi-3 Mini Q4_K_M → LangChain prompt → stream answer → unload

## Slide 7
04 — Methodology: MoC & Memory Management
Model of Computation — KPN
Kahn Process Network (KPN)
▸ Each module = sequential process
▸ Communication via FIFO disk channels
▸ No module starts before prior one terminates
Guarantees:
▸ Deterministic execution order
▸ No deadlock or race conditions
▸ Predictable peak memory bounds
▸ Single large object in RAM at any time
Memory Budget (Peak Stage Active)
OS + Runtime
200 MB
Ingestion
100 MB
Embedding
300 MB
Retrieval
80 MB
Generation
1400 MB
PEAK TOTAL
1680 MB
2 GB limit
Key strategies:
▸ Embedding unloaded before SLM loads
▸ FAISS index mmap-backed (paged on demand)
▸ gc.collect() at every module boundary
▸ n_ctx=512 caps KV-cache; watchdog at <100 MB free

## Slide 8
05 — Evaluation Plan
Dataset
▸ 10 embedded-systems datasheets / ARM manuals
▸ ~500 pages → 100 annotated QA pairs
▸ SQuAD 2.0 subset (200 technical QA questions)
▸ Query types: factoid, procedural, definition
Experimental Conditions
C1 — Baseline
2 GB RAM, 2 cores, Phi-3 Q4_K_M, FAISS
C2 — Memory-Stressed
1.5 GB RAM — tests OOM mitigation
C3 — No-RAG Ablation
SLM only, no retrieval — measures RAG gain
Metrics
System Metrics
Peak RAM
VmRSS via /proc/$PID/status
< 1.8 GB
Latency
Wall-clock, end-to-end
< 60 s
Tokens/sec
Generated tokens ÷ gen time
≥ 0.5
OOM Rate
Fraction of crashes / total
< 5%
RAG / QA Metrics
Recall@k
Top-k contains relevant chunk (k=1,3,5)
≥ 0.65 @3
F1 Score
Token F1 vs ground truth (SQuAD protocol)
≥ 0.40
Exact Match
Binary score for factoid answers
—

## Slide 9
06 — Embedded System Design Considerations
🧠 Resource Constraints
▸ 2 GB RAM hard ceiling enforced by QEMU
▸ KPN MoC ensures single active module
▸ Peak ~1.68 GB — 320 MB headroom
⚡ Real-Time Constraints
▸ No hard real-time requirement
▸ Soft target: ≤ 60 s end-to-end
▸ Latency bucketed by output length
🔒 Security
▸ -net none: zero network egress
▸ SHA-256 model integrity check
▸ LUKS encryption recommended in prod
🛡️ Reliability
▸ OOM watchdog at < 100 MB free RAM
▸ Graceful pipeline termination on risk
▸ ≥ 95% query success target
🌿 Energy Efficiency
▸ No continuous cloud round-trips
▸ CPU-only inference — no GPU power
▸ Significant carbon footprint reduction
🔄 Reproducibility
▸ setup.sh deterministic build script
▸ Fixed model checksum verification
▸ Docker/QEMU image for replication

## Slide 10
Semester Timeline
Wk 1–2
Requirements & Spec
Constraints, metrics, dataset selection
Wk 3
Architecture Design
Data flow, memory budget, software design
Wk 4
QEMU Setup
ARM64 env, 2 GB limit, verify boot
Wk 5
SLM Deployment
Phi-3 Mini Q4_K_M, baseline inference
Wk 6
Ingestion + Embedding
IngestionModule, EmbeddingModule, FAISS
Wk 7
★ Proposal + Retrieval
Extended proposal submission + RetrievalModule
Wk 8
Full Pipeline
GenerationModule integrated, end-to-end test
Wk 10
Profiling & Evaluation
Memory, latency, OOM, RAG quality
Wk 12
Optimization
Chunk size, k-value, quantization tuning
Wk 14
Final Report
Ablation study, conclusion, submission

## Slide 11
Thank You
Hüseyin Eren Doğan - N25123065
CMP720 Embedded System Design – Spring’26
Hacettepe University - Aselsan